## Slide 1: 4.1 TWC Operations: Seismic Monitoring in the Caribbean
Christa von Hillebrandt-Andrade
NOAA-NWS Caribbean Tsunami Warning Program
Regional Training Workshop on Pacific Tsunami Warning Center Enhanced Tsunami Products for ICG/CARIBE EWS
31 October – 02 November, 2017
Cartagena, Colombia

## Slide 2: CARIBE EWS Recommendations
Minimum seismic network performance requirements for initial earthquake locations:
  1) Earthquake detection within 1 minute
  2) Minimum magnitude threshold M=4.5.
Real Time Data Sharing Recommendations
  MS should share seismic data with US TWC – PTWC (primary TSP) and NTWC (backup for PTWC)
  MS should share data with PRSN, for their operations and relaying to US TWC
  MS should share data with IRIS (Incorporated Research Institutions for Seismology) for tsunami research, also a non guaranteed source of real time data

## Slide 4
Follow up by CTWP of stations status, data availability and improvements in the number of contributing stations

## Slide 5: CARIBE EWS Support
Working Group on Tsunami Monitoring and Detection, Chaired by Nestor Luque
Regional training for seismic network operators – every 2 – 3 years
CTWP produces monthly reports on seismic data availability
CTWP hosts bimonthly virtual meetings of seismic network operators

## Slide 6: Seismic Stations March 2017
Notes: Seismic stations in the Caribbean. Status from CTWP.

## Slide 7: Mexican Seismic Network Station

## Slide 8
2006
2017
Magnitude threshold : goal 4.5

## Slide 9
2006
2017
Detection time : goal 1 minute

## Slide 10
http://www.iris.washington.edu/gmap/_CARIBE-EWS
Notes: On IRIS a virtual seismic network was established to aggregate all the information from registered Caribbean seismic stations, whether or not data has been archived at the Data Management Center (http://www.iris.edu/gmap/_CARIBE-EWS). Among other services, IRIS offers a webservice to track and follow changes that have occurred in the metadata stored in their facility (http://service.iris.edu/irisws/metadatachange/1/), even if no data are available

## Slide 11
Chart: Status of Caribe EWS Core Seismic Stations
| Jun-17 | Jul-17 | Aug-17 | Sep-17
Contributing Real Time | 0.9375 | 0.9375 | 0.93714 | 0.9375
Existing | 0.034091 | 0.034091 | 0.034286 | 0.034091
Planned | 0.011364 | 0.011364 | 0.011429 | 0.011364
Gap | 0.0056818 | 0.0056818 | 0.0057143 | 0.0056818
Non-operational | 0.011364 | 0.011364 | 0.011429 | 0.011364

## Slide 12
Chart: Status of Caribe EWS Core Seismic Stations in the Caribbean
| Jun-17 | Jul-17 | Aug-17 | Sep-17
Contributing Real Time | 0.94074 | 0.94074 | 0.94074 | 0.93382
Existing | 0.044444 | 0.044444 | 0.044444 | 0.044118
Planned | 0.0074074 | 0.0074074 | 0.0074074 | 0.0073529
Gap | 0 | 0 | 0 | 0.0073529
Non-operational | 0.0074074 | 0.0074074 | 0.0074074 | 0.0073529

## Slide 13
Notes: Data availability in US-NTWC (March 2017, CTWP). This graph shows only the ratio of available stations over all the contributing stations.

## Slide 14
Chart: Data Availability for Contributing- RTX Stations at IRIS (Jun - Sep 2017)
| 90%-100% | 80%-89.9% | 70%-79.9% | 60%-69.9% | 50%-59.9% | 40%-49.9% | 30%-39.9% | 20%-29.9% | 10%-19.9% | 0%-9.9%
Jun 17 | 0.64844 | 0.046875 | 0.023438 | 0.015625 | 0.015625 | 0.0078125 | 0.0625 | 0 | 0 | 0.17969
Jul 17 | 0.6378 | 0.070866 | 0.023622 | 0.015748 | 0.015748 | 0.015748 | 0.015748 | 0 | 0 | 0.20472
Aug 17 | 0.70297 | 0.029703 | 0.059406 | 0 | 0.009901 | 0.019802 | 0.009901 | 0 | 0 | 0.16832
Sep 17 | 0.62745 | 0.0098039 | 0.039216 | 0.068627 | 0.0098039 | 0.0098039 | 0.0098039 | 0.0098039 | 0.039216 | 0.17647
Notes: Data availability for Contributing-RTX stations at IRIS (May – August 2017)

## Slide 15
Chart: 5 min Latency for Contributing-RTX Stations at US-NTWC (Jun - Sep 2017)
| 90%-100% | 80%-89.9% | 70%-79.9% | 60%-69.9% | 50%-59.9% | 40%-49.9% | 30%-39.9% | 20%-29.9% | 10%-19.9% | 0%-9.9%
Jun 17 | 0.61905 | 0.063492 | 0.0079365 | 0.031746 | 0.0079365 | 0.0079365 | 0.047619 | 0.02381 | 0.015873 | 0.1746
Jul 17 | 0.22131 | 0 | 0 | 0.016393 | 0.0081967 | 0.0081967 | 0.032787 | 0.032787 | 0.07377 | 0.60656
Aug 17 | 0.65041 | 0.065041 | 0.03252 | 0.02439 | 0.0081301 | 0.02439 | 0 | 0.0081301 | 0 | 0.18699
Sep 17 | 0.43307 | 0.12598 | 0.03937 | 0.03937 | 0.055118 | 0.031496 | 0.031496 | 0.007874 | 0.031496 | 0.20472
Notes: 5 minute latency for Contributing-RTX stations at US-NTWC (May – August 2017)

## Slide 16
Chart: Uptime Percentage for Contributing-RTX Stations at PTWC (Jun - Sep 2017)
| 90%-100% | 80%-89.9% | 70%-79.9% | 60%-69.9% | 50%-59.9% | 40%-49.9% | 30%-39.9% | 20%-29.9% | 10%-19.9% | 0%-9.9%
Jun 17 | 0.51064 | 0.074468 | 0.031915 | 0.021277 | 0 | 0.021277 | 0.085106 | 0.042553 | 0.010638 | 0.20213
Jul 17 | 0.56383 | 0.10638 | 0.021277 | 0.010638 | 0.010638 | 0.010638 | 0.010638 | 0 | 0 | 0.26596
Aug 17 | 0.57895 | 0.052632 | 0.031579 | 0.021053 | 0.031579 | 0.031579 | 0 | 0.010526 | 0.010526 | 0.23158
Sep 17 | 0.26374 | 0.10989 | 0.021978 | 0.26374 | 0.010989 | 0.010989 | 0.032967 | 0.021978 | 0.043956 | 0.21978
Notes: Uptime percentage for Contributing-RTX stations at PTWC (May – August 2017)

## Slide 17
Chart: 1 min Latency for Contributing-RTX Stations at PRSN (Jun - Sep 2017)
| 90%-100% | 80%-89.9% | 70%-79.9% | 60%-69.9% | 50%-59.9% | 40%-49.9% | 30%-39.9% | 20%-29.9% | 10%-19.9% | 0%-9.9%
Jun 17 | 0.43925 | 0.11215 | 0.11215 | 0.093458 | 0.028037 | 0.0093458 | 0.028037 | 0.0093458 | 0.0093458 | 0.15888
Jul 17 | 0.43925 | 0.17757 | 0.084112 | 0.093458 | 0.0093458 | 0 | 0.018692 | 0 | 0 | 0.17757
Aug 17 | 0.50617 | 0.11111 | 0.049383 | 0.08642 | 0 | 0 | 0 | 0 | 0 | 0.24691
Sep 17 | 0.012987 | 0 | 0 | 0.45455 | 0.090909 | 0.077922 | 0.077922 | 0.012987 | 0.038961 | 0.23377
Notes: One minute latency for contributing-RTX stations at PRSN (May – August 2017)

## Slide 18
Chart: Percentage Caribe Stations Contributing RTX for September 2017
| 90-100 % | 50-90% | 0-50% | Not Reported
PRSN | 0.007874 | 0.33071 | 0.26772 | 0.3937
NTWC | 0.25984 | 0.22047 | 0.28346 | 0.23622
PTWC | 0.18898 | 0.29134 | 0.23622 | 0.28346
IRIS | 0.29921 | 0.094488 | 0.1811 | 0.4252

## Slide 19: Metadata quality check
Seismic metadata is crucial for correct threat level assessment (EQ location and magnitude)
Metadata quality check performed on IRIS and TSPs metadata
Automatic identification of problems using spectral representation
Just a few minor problems identified at IRIS repository
More questions raised by the on-going work on TSPs metadata

## Slide 20: Continuous GPS network
COCONet and TLALOCNet projects installations almost completed
1Hz high rate real-time GNSS capabilities for 52 stations in the Caribbean and 15 in Mexico
COCONet community workshop in Punta Cana in May 2016
Real-time GNSS stations requirements proposed

## Slide 21: GPS integration into the Mexican Seismic Network

## Slide 22
Continuous GNSS stations

## Slide 23
Real-time GNSS network

## Slide 24
Real-time GNSS applications
Courtesy of Gerald Bawden, NASA

## Slide 25
Real-time GNSS applications :
wave heigh estimation (2cm detection threshold)
Courtesy of Giovanni Occhipinti, IPGP

## Slide 26: Thanks to all the Seismic Networks that Contribute Data to the CARIBE EWS
Regional Training Workshop on Pacific Tsunami Warning Center Enhanced Tsunami Products for ICG/CARIBE EWS
31 October – 02 November, 2017
Cartagena, Colombia

## Slide 27: Thank You
Christa von Hillebrandt-Andrade
NOAA-NWS Caribbean Tsunami Warning Program
Regional Training Workshop on Pacific Tsunami Warning Center Enhanced Tsunami Products for ICG/CARIBE EWS
31 October – 02 November, 2017
Cartagena, Colombia